## Slide 1: CMSIS-Toolbox: Basis for next generation software tooling
Keil MDK – Version 6
Best-in-class embedded development system for Cortex-M microcontrollers
Command-Line and IDE workflows based on CMSIS-Toolbox
Arm C/C++ Compiler with FuSa certification
Based on CMSIS software standards
Host Support: Windows, Linux, Mac OS – and Cloud
Arm Virtual Hardware – FVPs
Precise simulation models of Cortex-M device sub-systems
Designed for complex software verification and testing
Enables test automation of diverse software workloads
Part of CI/CD and MLOps development flows
Supports A/B performance comparisons using CMSIS-View Event Recorder timing statistics
csolution project
Software Packs
CMSIS-Toolbox
cbuild: Build Invocation
Command-line workflow
Visual Studio Code IDE
Arm Virtual Hardware
Cortex-M0..M85
SIMD, Helium
Memory
DMA
Virtual I/O
Data Streaming
Ethos-U55/U65
microNPU
Peripherals
Ethernet, UART,…
Debug Interface
Event Recorder
Resources
microNPU
Test scripts
CI/CD integration
Integrations
Cloud Service
GitHub
Desktop tools
*.cproject.yml source files and SW components
Device/Board Generic Software
*.csolution.yml Target and Build Parameters

## Slide 2
Output Files
Input Files
Software Packs
*.rzone (optional) Defines system resources
*.csolution.yml Target (Device, Board) Build (Debug, Release)
*.cproject.yml Manages independent projects
Run-Time Environment (RTE) (*.c / *.h files with config information)
*.clayer.yml Defines re-usable project parts
Device Family Pack (DFP)
Defines device properties
Board Support Pack (BSP) Defines board properties
CMSIS Project Manager
Project Build Files *.cprj for CMSIS-Build
Generic Software Packs with drivers, middleware, etc.
Project Resource Files *.fzone for template engines
1
2
3
4
*.cdefault.yml Global Settings (Toolchain)

## Slide 3
Output Files
Input Files
Software Packs
*.rzone (optional) Defines system resources
*.csolution.yml Target (Device, Board) Build (Debug, Release)
*.cproject.yml Manages independent projects
Run-Time Environment (RTE) (*.c / *.h files with config information)
*.clayer.yml Defines re-usable project parts
Device Family Pack (DFP)
Defines device properties
Board Support Pack (BSP) Defines board properties
csolution CLI tool
Project Build Files *.cprj for CMSIS-Build
Generic Software Packs with drivers, middleware, etc.
Project Resource Files *.fzone for template engines
1
2
3
4
*.cdefault.yml Global Settings (Toolchain)
future extension
Generator
legacy
*.genlayer.yml Defines generated project parts
*.cbuild.yml Build information
future extension

## Slide 4
Default options for AC6, GCC, IAR, LLVM
Output Files
csolution project
Software Packs
*.csolution.yml Target (Device, Board) Build (Debug, Release)
*.cproject.yml Manages independent projects
Run-Time Environment (RTE) (config files*.c / *.h)
*.clayer.yml Defines re-usable project parts
Device Family Pack (DFP)
Defines device properties
Board Support Pack (BSP) Defines board properties
csolution CMSIS Project Manager
*.CPRJ Project Build for CMSIS-Build
Generic Software Packs with drivers, middleware, etc.
cdefault.yml Global Toolchain Settings
legacy
*.cbuild-idx.yml *.cbuild.yml Build information
Note: Optionally memory information for Linker Scatter Files is generated.
Pack lock and context selection for build
*.cbuild-pack.yml *.cbuild-set.yml

## Slide 5
Generator Information
Generator Output
*.ioc Generator Project
*.c/*.h generated source files
<project>. cbuild-gen.yml
<project>. cgen.yml Import data for CMSIS-Toolbox
cbridge Generator Bridge
*.cbuild-gen-idx.yml
CubeMX Generator

## Slide 6
csolution CMSIS Project Manager
Debugger
Flash Programmer
OTA/Cloud Service
cbuild-set.yml Project context set

## Slide 7
Default compiler options for AC6, GCC, IAR
Output Files
csolution project
Software Packs
*.csolution.yml Target (Device, Board) Build (Debug, Release)
*.cproject.yml Manages independent projects
Run-Time Environment (RTE) (config files*.c / *.h)
*.clayer.yml Defines re-usable project parts
Device Family Pack (DFP)
Defines device properties
Board Support Pack (BSP) Defines board properties
cbuild CMSIS Project Manager
Generic Software Packs with drivers, middleware, etc.
cdefault.yml Global Toolchain Settings
*.cbuild-idx.yml *.cbuild.yml Build information
Note: Optionally memory information for Linker Scatter Files is generated.
*.cbuild-idx.yml *.cbuild.yml Build information

## Slide 8
Output Files
csolution project
Software Packs
*.rzone (optional) Defines system resources
*.csolution.yml Target (Device, Board) Build (Debug, Release)
*.cproject.yml Manages independent projects
Run-Time Environment (RTE) (*.c / *.h files with config information)
*.clayer.yml Defines re-usable project parts
Device Family Pack (DFP)
Defines device properties
Board Support Pack (BSP) Defines board properties
csolution CLI tool
Project Build Files *.cprj for CMSIS-Build
Generic Software Packs with drivers, middleware, etc.
Project Resource Files *.fzone for template engines
1
2
3
4
*.cdefault.yml Global Settings (Toolchain)
future extension
Generator
legacy
*.cgen.yml Defines generated project parts
*.cbuild.yml Build information
future extension

## Slide 9
Read previous *.cprj files to check for config file version changes
Control config file versions in case of updated software packs
Read Software Packs and csolution project files
Process data
Read previous *.cprj file to identify the config file versions previously used
Compare versions of “config” files, notify if updates are made (define rename process of config files)
Check if new *.cprj file is different from old config files; if it differs rename existing *.cprj to backup version; write new *.cprj file
Q: do we need a status file, perhaps for an IDE flow?
*.rzone (optional) that defines System Resources
*.csolution.yml Defines Target Application
*.cproject.yml Manages independent projects
Run-Time Environment (RTE) (*.c / *.h files with config information)
*.clayer.yml Defines re-usable project parts
Device Family Pack (DFP)
that defines Device Properties
Board Support Pack (BSP) that defines Board Properties
CMSIS Project Manager
Project Files *.cprj for CMSIS Build
csolution project
Software Packs
[default.]csettings.yml Global Settings (Toolchain, Device)
Generic Software Packs with drivers, middleware, etc.
Project Resource Files *.fzone for template engines
Output Files

## Slide 10: Multi-Project Build Process: IDE and CLI
*.csolution.yml Defines Target Application
csolution Project setup: defines tools, target, components, files, and current list of context that should be build.
csolution project
Build Control Files
*.cbuild-set.yml Defines context set of Application
cbuild (CLI)
Invokes csolution
When csolution project files are newer (context-set of *.cbuild-idx.yml defines scope) Invokes cbuild-gen for build process
<context>.cbuild.yml Build information for a project context
IDE
When setup in context manager is changed (or items modifed), csolution is called
When build is invoked, cbuild-gen is called.
Introduce `context-set`: defines the selected context for application
Items are stored in csolution project files
toolchain
device, board,
build-type, target-type
components
files
options
cbuild-gen
Build Process: uses the build control files to generate the output (via CMake, …)
csolution command-line defines context-set:
csolution convert HelloWorld.csolution.yml --context HelloWorld_cm0plus.Debug+FRDM-K32L3A6 --context -HelloWorld_cm4.Release+FRDM-K32L3A6

## Slide 11: Application Software – from Virtual to Physical Hardware
User Application Code
Virtual Layer
IoT/ML Software Platform
Provide evidence of correctness on Arm Virtual Hardware Target and Physical Hardware
Event Log file
User Application Code
Board Layer
IoT/ML Software Platform
Event Log file
Device SDK with configuration
User Application Code
Target Layer
IoT/ML Software Platform
Event Log file
Device SDK with configuration
More Software
More Drivers
Virtual Drivers
HW Drivers
Real I/O via test equipment
Real I/O via user peripherals
HW Drivers
Unit & Integration Testing on Virtual Hardware or Physical Hardware Boards
Deployment and System Testing on Production Hardware
Essentially the same event logs are generated across the different deployments. This ensures correctness.
Simulated I/O via Python scripts and stimuli files
Notes: Potential key customer: DSP Concepts. See email exchange:
From: Paul Beckmann <pbeckmann@dspconcepts.com> Sent: Wednesday, April 7, 2021 9:05 PM To: Reinhard Keil <Reinhard.Keil@arm.com> Subject: Re: Compiler comparison / Feedback on Audio API interface
Hi Reinhard,
We are our testing with MDK V5.31.0.0. Here is the detailed info:
For IAR, we used v8.50.1. For GCC, it was the version included with the ST tools. Not sure exactly which version this was.
We have done further benchmarking across different signal processing operations. I picked this one because it was a recent issue with a customer and highlights how GCC can be slow. For other kernels, the cycle counts are comparable.
Being able to run on the FVP would be very interesting for us. I see several advantages:
We can optimize and profile for cores before they are publicly available. For example, we are getting requests for M55 performance numbers but there are no announced CPUs.
Get accurate measurements of system level issues. Caching and memory accesses have a huge impact.
Could fit with our continuous integration plans so that we don't have to (always) test on external hardware.
We are speaking with Reed Hinkel about "cloud based profiling". I would like our customers to create a design in Audio Weaver and then upload the design to our website for profiling. They can select which processors to run on and then get detailed results showing where resources are consumed. The VFP would be ideal for this.
I also had one of my firmware engineers review the SAI interface. I'll provide all of his comments and you can see what is relevant:
It is well written and to make sure I understand it, low-level drivers must be written depending on the device.
  You have to kickstart the driver with calls to ARM_SAI_Receive() or ARM_SAI_Send() which are non-blocking.
  A callback function is registered during init called ARM_SAI_SignalEvent(event) which is called when the above completes with respective bits in the parameter "event" for each.
  ARM_SAI_Receive() or ARM_SAI_Send() mention that DMA is typical, but I am not sure if those two calls can be one time only and then the guts of the driver can provide calls to ARM_SAI_SignalEvent(event) on each DMA interrupt afterward. If yes, then it can work with our BSP's.
  The protocols cover about everything with User Defined Protocol allowing for generic TDM configuration.
    They are missing specification of left or right adjusted data and now to save captured data in memory. For instance if the data is 24-bits, is it saved right adjusted with sign extension or left adjusted?
    In general, you may capture even 16-bit data and want to save it in 32-bit memory left or right adjusted.
  The same API and supported protocols should include PDM (DMIC) input. The RT685 and NXP PDM IP in general have a means to convert to I2S, but that may not be on all parts and should not be necessary.
    Most devices have multiple stereo PDM ports that can capture data and send to two different DMA channels (left and right).
    This API seems to support single stream, interleaved, not multi-stream from one device. Is that correct?
  The documentation is not clear how you mask the TX event, bot allow the RX event and so on. Guessing it is in there.

## Slide 12: Multi-Project Requirements
Project D
Project B
Project A
Separate projects independently developed; combined in a multi-project workspace
Security
Storage
Crypto
Attestation
Device / Board HAL
RTOS
User Application
Cloud
Connector
Secure Network
Interface
Secure Boot
ML Library
ML Data
UX Graphic
Images
Control Algorithm
Processor #1
Processor #2
Project C

## Slide 13: Software Layers Group Pre-configured Software Components
RTOS Layer
App Layer
Socket Layer
IoT for Cortex-M – reference examples for many evaluation kits
Board Layer
MCU
Board
LED
Sensor inputs
Display
CMSIS-Driver-VIO
Virtual I/O
CMSIS-RTOS2
Example Application Code
Trusted Firmware-M (TF-M)
implements Security
Storage
Crypto
Attestation
Secure Boot
TrustZone Security
FreeRTOS, RTX, …
SPI
I2C
USART
WiFi
CMSIS-Driver
SPI, UART, (Ethernet)
Cloud Connector + Security
IoT Socket + Communication Stack
Peripherals covered by real CMSIS-Driver or VIO (Virtual I/O)
Timers
Analog
...
User Code
Specialized Peripherals
Device SDK with configuration
Module Layer
WiFi

## Slide 14: Scenarios to consider
csolution
cproject #1
cproject #2
clayer for common board settings
csolution
cproject #1 runs on CPU #1
cproject #2 runs on CPU #2
clayer #1 for board API
clayer #2 for board API
common RTE settings (includes generator files)
Projects that share a layer with common configuration
Layers that partly share a common configuration
RTE settings (includes generator files)

## Slide 15: CubeMX location of generated files
csolution
cproject #1
cproject #2
clayer directory
csolution
cproject #1 runs on CPU #1
cproject #2 runs on CPU #2
Require common directory for
generated files
“Simple” Projects that share a layer with common configuration
TrustZone or Multicore projects
./RTE/Device/$D contains generated files
csolution
csolution
cproject directory
./RTE/Device/$D contains generated files

## Slide 16: CubeMX location of generated files
clayer directory
csolution
cproject #1 runs on CPU #1
cproject #2 runs on CPU #2
Require common directory for
generated files
TrustZone or Multicore projects
clayer CPU #1
clayer CPU #2

## Slide 17: CSolution / CBuild: Generator Workflow
Steps for component selection and configuration
User selects components
in `*.cproject.yml` under `components:`
When this are components that require generation, user is notified about the requirement to run a generator and users the CSolution Run command.
Run a “Generator” for a list of components.
CSolution generates `*.cgen.yml` that provides the list of user-selected components.
User runs Generator
`*.cgen.yml` provides the input to the Generator with a list of selected components
Configuration is done.
  Interactive mode (where a settings file is generated)
  Remote mode (where a settings file is an input)
Generator creates the “myGen.gpdsc” that informs the CSolution tool about (a) the fact that a component is configured and has generated code, (b) additional components that are the result of some user configuration.
Discussion: is a component list or a dependency list
Generator might be VS Code plugin or web based.
User creates CBuild output with CSolution
Both `*.cproject.yml` “myGen.gpdsc” and read by Csolution and create the complete list of selected components.
If “myGen.gpdsc” does not contain component information about a component with `genId` that is selected in `*.cproject.yml` the generator configuration is incomplete. This can happen when a component is added at a later step.
Likewise the Generator should remove components that are no longer required. An indicator is needed. (NOT SOLVED YET)

## Slide 18: IoT Workshop Example - Structure
Reference Application Framework: map many applications to many boards
IoT Reference Application using RTOS Kernel
PSA Interface
Device/Board Abstraction Layer
Security Firmware
SW Building Blocks
Should come from multiple vendors. Requirement for standardized interface between the components (Open-CMSIS-CDI)
Reference Application: should be tested with a CI system against a standardized CDI framework
Should run (within reason) on many different existing v8M and v7M devices (TrustZone optional)
Should include OTA services with standardize interfaces
Future variants of the Framework should also support other application types (DSP, ML, Graphics)
Designed for `csolution` tool
Examples use Open-CMSIS-Pack and the csolution workflow with layers
Layer type names should be descriptive, i.e. board, socket, security
Examples are used to fine-tune the csolution workflow (see next slide)
Interface requirements between cproject/clayer files should be described
Final design is that layers are provided by software packs
Other Requirements:
Defined Startup/Call Sequence (see https://github.com/MDK-Packs/CB_Lab4Layer/tree/master/layer)
Example: https://github.com/MDK-Packs/CB_Lab4Layer/blob/master/layer/Board/MIMXRT1064-EVK/main.c
Socket Layer (IoT Socket -> WiFi or Ethernet)
CMSIS-Driver API
IoT Socket API
Objectives
Re-use existing packs from AWS and NXP
provide feedback when required
Define the overall structure of CMSIS-Packs, i.e. for
TF-M
mbedTLS
AVH Corstone-300 BSP
Board BSP (exemplified on STM32U5, NXP)

## Slide 19: Opportunity: Packs give flexibility to the SW Eco-system
Flexible Development Workflows with Open-CMSIS-Pack
Catalog of software packs
MyProject *.csolution.yml *.cproject.yml
Arm Virtual Hardware
+
Private software packs
+
CLI Tools
Support: Win/Linux/Mac
Integrate with: VS Code, Keil Studio Cloud
Other tool integrations:
Arm DS, Keil MDK, IAR EW-Arm, Eclipse
NXP?
ST?
Boards or Devices
AVH Integrates into:
CI, DevOps, MLOps systems (i.e. GitHub)
Keil MDK, Arm DS, IAR EW-Arm
Keil Studio Cloud
AVH Supports:
CI Validation
Evaluation
Training
Platform for Reference Applications:
Many different boards???
Standard Software exposed to developers:
Web portals
Inside IDEs
Confidential software
Git repo for development
Released software with versioning
CMSIS Toolbox
Compiler support
GCC
Arm Compiler
IAR Compiler
github.com/Open-CMSIS-Pack

## Slide 20: Linker Script File and Startup Code (Toolchain independent)
Linker Script File
C Preprocessor
Final Linker Input Script
A <regions>.h file specifies the available memory.
If this file does not exist, it is generated based on information in the software packs.
A Linker Script File can be provided using the `linker:` node.
If no Linker Script File is provided, compiler specific script file templates from .\ect directory of CMSIS-Toolbox are used.
<regions>.h Device (and Board) Memory Definitions

## Slide 21
RTE Directory
Project Area
csolution project
Software Packs
*.csolution.yml Target (Device, Board) Build (Debug, Release)
*.cproject.yml Manages independent projects
*.clayer.yml Defines re-usable project parts
csolution tool
*.cprj Build Information
*.pdsc Pack Metadata
*.cbuild.yml Build Information
*.cbuild-idx.yml Overall description with project index
Component Config Files
RTE_ components.h
Pre-include Files
Component Config Files
cbuildgen tool called by cbuild
*.default.yml Compiler selection and toolchain default settings
Cbuild2cmake tool called by cbuild

## Slide 22
*.cprj Build Information
cmakeLists.txt
compiler_name. <version>.cmake
CMake
build.ninja
Ninja
cbuildgen

## Slide 23
cbuild
cpackget
csolution
buildmgr
CMake
Ninja
csolution project *.csolution.yml
*.cproject.yml
*.clayer.yml
Software Packs Device Family Pack
Board Support Pack
Generic Software Packs
Build Information list of source files, packs, tool options, etc.
User source code Configuration files Linker Scripts
Build Output Elf/Dwarf files Map files
etc.

## Slide 24
Arduino Shield
D0
D1
D2
D3
D4
D5
D6
D7
D8
D9
D10
D11
D12
D13
GND
AREF
D20
D21
SDA
SCL
I2C
RXD
TXD
UART
D19
D18
D17
D16
D15
D14
VIN
GND
GND
+5V
+3V3
Reset
IOREF
NC
A5
A4
A3
A2
A1
A0
CIPO
SCK
SS
COPI
SPI
SCL
SDA
I2C-Alt
Analog
Digital
Communication

## Slide 25: Distribution of Reference Applications
Sensor SDK Pack
BSP Pack
Reference Application (<sensor>.csolution.yml / <sensor>.cproject.yml)
Layer Type: Board (<board-name>.clayer.yml)
Driver APIs
Layer Type: Shield (<shield-name>.clayer.yml)
Shield-specific API
Example: Sensor SDK Pack (github.com/RobertRostohar/NXP_Sensor_SDK) that contains:
Agnostic middleware for a sensor that is configurable (part of the Reference Application)
Board/Device agnostic examples that use this middleware (part of the Reference Application)
One or more Shield layers that provides configuration settings for the agnostic middleware
Board Layers are provided by a Board Support BSP Pack that is board specific
Sensor SDK Pack PDSC:
<example> describes Reference Application
<clayer> describes <shield-name>.clayer.yml
BSP Pack PDSC:
<clayer> describes <board-name>.clayer.yml

## Slide 27: IoT Workshop Example - Structure
Reference Application Framework: map many applications to many boards
Reference Application (*.cproject.yml)
PSA Interface
Layer Type: Board (<board-name>.clayer.yml)
Security Firmware
Layer Type: Socket Network Connectivity
CMSIS-Driver API
IoT Socket API
Layer Type: Shield (<shield-name>.clayer.yml)
Shield-specific API
Layer Type: RTOS RTOS Functionality
CMSIS-RTOS2 API
Layer Type: Stream Sensor Middleware
Data Stream API
Security Boundary

## Slide 28: Roadmap H1’2023 – CMSIS-Toolbox 2.0
Review proposals and agree on implementation timeline (until 15. Feb 2023)
Identify missing features for integration into VS Code
Work on Installer that (a) is stand-along for Linux, (b) installs CMSIS-Toolbox to VS Code
Define an overall multi-project workflow that starts from *.cbuild-idx.yml (as cbuild input file)
Complete Generator Workflow
Implement Gaps:
  csolution list config #142,
Out of scope (todo later in 2023)
CMSIS-Zone integration and resource management proposal
Command for batch delete #143

## Slide 29
Software Application
Software Packs
*.csolution.yml Target and Build Parameters
*.cproject.yml source files and SW components
csolution Project Manager
Device/Processor Information
Software Building Blocks

## Slide 30
User Application Code
Virtual Layer
IoT/ML Software Platform
Event Log file
User Application Code
Board Layer
IoT/ML Software Platform
Event Log file
Device SDK with configuration
User Application Code
Target Layer
IoT/ML Software Platform
Event Log file
Device SDK with configuration
More Software
More Drivers
Virtual Drivers
HW Drivers
Real I/O via test equipment
Real I/O via user peripherals
HW Drivers
Unit & Integration Testing on Virtual Hardware or Physical Hardware Boards
Deployment and System Testing on Production Hardware
Essentially the same event logs are generated across the different deployments. This ensures correctness.
Simulated I/O via Python scripts and stimuli files
Target Hardware Abstraction
Notes: Potential key customer: DSP Concepts. See email exchange:
From: Paul Beckmann <pbeckmann@dspconcepts.com> Sent: Wednesday, April 7, 2021 9:05 PM To: Reinhard Keil <Reinhard.Keil@arm.com> Subject: Re: Compiler comparison / Feedback on Audio API interface
Hi Reinhard,
We are our testing with MDK V5.31.0.0. Here is the detailed info:
For IAR, we used v8.50.1. For GCC, it was the version included with the ST tools. Not sure exactly which version this was.
We have done further benchmarking across different signal processing operations. I picked this one because it was a recent issue with a customer and highlights how GCC can be slow. For other kernels, the cycle counts are comparable.
Being able to run on the FVP would be very interesting for us. I see several advantages:
We can optimize and profile for cores before they are publicly available. For example, we are getting requests for M55 performance numbers but there are no announced CPUs.
Get accurate measurements of system level issues. Caching and memory accesses have a huge impact.
Could fit with our continuous integration plans so that we don't have to (always) test on external hardware.
We are speaking with Reed Hinkel about "cloud based profiling". I would like our customers to create a design in Audio Weaver and then upload the design to our website for profiling. They can select which processors to run on and then get detailed results showing where resources are consumed. The VFP would be ideal for this.
I also had one of my firmware engineers review the SAI interface. I'll provide all of his comments and you can see what is relevant:
It is well written and to make sure I understand it, low-level drivers must be written depending on the device.
  You have to kickstart the driver with calls to ARM_SAI_Receive() or ARM_SAI_Send() which are non-blocking.
  A callback function is registered during init called ARM_SAI_SignalEvent(event) which is called when the above completes with respective bits in the parameter "event" for each.
  ARM_SAI_Receive() or ARM_SAI_Send() mention that DMA is typical, but I am not sure if those two calls can be one time only and then the guts of the driver can provide calls to ARM_SAI_SignalEvent(event) on each DMA interrupt afterward. If yes, then it can work with our BSP's.
  The protocols cover about everything with User Defined Protocol allowing for generic TDM configuration.
    They are missing specification of left or right adjusted data and now to save captured data in memory. For instance if the data is 24-bits, is it saved right adjusted with sign extension or left adjusted?
    In general, you may capture even 16-bit data and want to save it in 32-bit memory left or right adjusted.
  The same API and supported protocols should include PDM (DMIC) input. The RT685 and NXP PDM IP in general have a means to convert to I2S, but that may not be on all parts and should not be necessary.
    Most devices have multiple stereo PDM ports that can capture data and send to two different DMA channels (left and right).
    This API seems to support single stream, interleaved, not multi-stream from one device. Is that correct?
  The documentation is not clear how you mask the TX event, bot allow the RX event and so on. Guessing it is in there.

## Slide 31
Target Hardware Abstraction
Target Hardware Abstraction

## Slide 32: Software components
A software component encapsulates a set of related functions.
Components should be substitutable by other components at design time.
Components can have dependencies on other components.
Software component
API headers
User code templates
Configuration files
Source code/
libraries
Documentation
Debug view
description
Interfaces to device peripherals or other software components
Interfaces to user application or other software components
  Provided Interfaces
  Required Interfaces
Notes: Requires you to think about the API of the software component

## Slide 33
- component: <2>
API header
Configuration files
Source code/
libraries
- component: <1>
API header
Configuration files
Source code/
libraries
- component: <1>
API headers
Configuration files
Source code/
libraries
Implementation #3
Implementation #2
Implementation #1
Source code/
libraries
Source code/
libraries
Source code/
libraries
Central API definition
API headers (Definition)
Documentation of API
- component: <2.C>
- component: <2.B>
- component: <2.A>
Source code/
libraries
Source code/
libraries
Source code/
libraries
Documentation
Notes: Requires you to think about the API of the software component

## Slide 34: Application example: TCP/IP network
Using network stack on STM32F407IG with internal MAC
Network:Socket:TCP
CMSIS Driver: Ethernet MAC
CMSIS Driver: Ethernet PHY
Network:Interface:ETH
Network:CORE
CMSIS:CMSIS-RTOS
Device Family Pack
Middleware Pack
CMSIS Pack
External Driver Pack
CMSIS:CORE
Device:Startup

## Slide 35: Class / Pack view
Device - pack vendor::DFP
CMSIS - pack Arm::CMSIS
CMSIS-Driver - pack vendor::HAL-Interface
CMSIS-Driver - pack Arm::CMSIS-Driver
CMSIS:RTOS2 RTOS&FreeRTOS - pack Arm::CMSIS-FreeRTOS
Network - pack: lwIP::lwIP
IoT Utility - pack MDK-Pack:IoT-Socket
IoT Client

## Slide 36: Software components – Taxonomy
Software component have these attributes that are used to identify them:
  Component Class (Cclass): examples are CMSIS, Device, File System
  Component Group (Cgroup): examples are CMSIS:RTOS, Device:Startup, File System:CORE
  Component Version (Cversion): the version number of the software component
Optionally, a software component may have additional attributes:
  Component Sub-Group (Csub): examples are CMSIS:RTOS:MyRTOS, Device:Driver USBD:Full-speed
  Component Variant (Cvariant): a variant of the software component: RTOS:FreeRTOS
  Component Vendor (Cvendor): the supplier of the software component
Notes: Requires you to think about the API of the software component

## Slide 37: Bundles
A bundle is a variant on the Cclass level.
It specifies the attributes Cclass, Cversion and optionally Cgroup and Cvendor for a collection of interdependent components.
Components within a bundle inherit the attributes set by the bundle and must not set these attributes again.
Bundles ensure consistency of attributes across multiple interworking components and restrict the mix and match of components within a Cclass from different solutions.
Bundle
Component A
Component B
Component C
Component X
Component Y
Component Z
Notes: Requires you to think about the API of the software component

## Slide 38: Bundles
In case multiple inter-dependent components that belong to the same Cclass form part of a solution, these can be grouped into a bundle (Cbundle).
A Cbundle specifies identical attributes Cclass, Cversion and optionally Cgroup and Cvendor for several components.
Components within a bundle inherit these attributes set by the bundle and cannot alter these attributes (for example component version).
Bundles ensure consistency of attributes across multiple interworking components and restrict the mix and match of components within a Cclass from different software packs.

## Slide 39: Relationships of packs and software components
Packs can require other packs to be available:
Components can have dependencies on other components; either from the same or from other packs:
Pack A
Version n
Pack B
Version m
Pack A, Version n
Component A
Component B
Component C
Pack B, Version m
Component A
Component B
Component C

## Slide 40: Central API Interface definition for software components
Implementation #3
Implementation #2
Software
component
Central API definition
A common problem: API headers evolve over time.
A central API definition shares header file and documentation of an API interface across multiple other software components to ensure consistency.
The API interface is distributed separate or as part of the software component that consumes this interface. The API header file is therefore.
An example is the CMSIS-Driver pack that contains various Ethernet and Flash drivers – all compatible with the CMSIS-Driver APIs that are published in the CMSIS Pack.
API headers
Source code/
libraries
Interfaces
API headers (Definition)
Implementation #1
Source code/
libraries
Source code/
libraries
Source code/
libraries
Documentation of API
Notes: Requires you to think about the API of the software component

## Slide 41: API components
An API is a special form of a software component that only defines a C/C++ Application Programming Interface (API).
An API does not contain the actual implementation (usually provided by source code or library files) and cannot be selected in a development tool. One example is the CMSIS-RTOS API, which is specified as part of CMSIS. However, the actual RTOS implementation is provided by different vendors.
An API consists of a name, a brief description as well as one or more header files. It references a document containing the specification of the API.

## Slide 42: Application example: TCP/IP network
Using network stack on STM32F407IG with internal MAC
Network:Socket:TCP
Ethernet MAC
Ethernet PHY
Network:Interface:ETH
Network:CORE
CMSIS:CMSIS-RTOS
Vendor 1 Pack
Middleware Pack
CMSIS Pack
External Driver Pack
CMSIS:CORE
Device:Startup

## Slide 43: Application example: TCP/IP network
Using network stack on an NXP LPC54108 without MAC
- component: Network:Socket:TCP
Ethernet MAC and PHY
CMSIS-Driver SPI
- component: Network:Interface:ETH
- component
Network:CORE
- component: CMSIS:CMSIS-RTOS2:RTX
- pack: Device Family Pack
- pack: Middleware Pack
- pack: CMSIS Pack
- pack: External Driver Pack
- component: CMSIS:CORE
Device:Startup

## Slide 44: Managing software components in a project
Pack manager creates RTE_Components.h header file
RTE_Components.h is an inventory file that contains:
CMSIS_device_header #define for generic access to the selected device’s header file
All defines that are generated out of components from PDSC files:
<component Cgroup="Core" Cversion="10.0.1" condition="FreeRTOS"> <description>Core components API (Kernel, Tasks, Semaphores, Mutexes, Queues)</description> <RTE_Components_h> #define RTE_RTOS_FreeRTOS_CORE /* RTOS FreeRTOS Core */ </RTE_Components_h> . . . </component>
Is added to the RTE_Components.h file:
/* * Auto generated Run-Time-Environment Component Configuration File * *** Do not modify ! *** */ #ifndef RTE_COMPONENTS_H #define RTE_COMPONENTS_H /* Define the Device Header File: */ #define CMSIS_device_header "ARMCM3.h“ #define RTE_RTOS_FreeRTOS_CORE /* RTOS FreeRTOS Core */ #endif /* RTE_COMPONENTS_H */

## Slide 45: Distribution of Reference Applications
Sensor SDK Pack
BSP Pack
Reference Application (<sensor>.csolution.yml / <sensor>.cproject.yml)
Layer Type: Board (<board-name>.clayer.yml)
Driver APIs
Layer Type: Shield (<shield-name>.clayer.yml)
Shield-specific API
Example: Sensor SDK Pack (github.com/RobertRostohar/NXP_Sensor_SDK) that contains:
Agnostic middleware for a sensor that is configurable (part of the Reference Application)
Board/Device agnostic examples that use this middleware (part of the Reference Application)
One or more Shield layers that provides configuration settings for the agnostic middleware
Board Layers are provided by a Board Support BSP Pack that is board specific
Sensor SDK Pack PDSC:
<example> describes Reference Application
<clayer> describes <shield-name>.clayer.yml
BSP Pack PDSC:
<clayer> describes <board-name>.clayer.yml

## Slide 46: Distribution of Reference Applications
MDK Middleware Pack
BSP Pack
Reference Application Example
Layer Type: Board (<board-name>.clayer.yml)
Driver APIs
USB Device
RTOS
HID Class
CMSIS-View
connections:
- connect: USB Device HID
consumes:
- CMSIS_USB_Device
- CMSIS_VIO
connections:
- connect: Board with USB
provides:
- CMSIS_USB_Device
- CMSIS_VIO

## Slide 47: Header File Structure
CMSIS_target_header Driver configuration
Device Registers
Reference Application
Hardware Abstraction
Driver implementation
Driver API Shim Interface
CMSIS_shield_header Shield configuration
CMSIS_target_header Driver configuration
Device Registers
Reference Application
CMSIS_shield_header Shield configuration
CMSIS_device_header Processor and Peripherals
STM32 HAL Drivers
CMSIS_device_header Processor and Peripherals
CMSIS-Driver API header files
CMSIS-Driver API header files

## Slide 48
Driver API Shim Interface
CMSIS_target_header Driver configuration
Device Registers
Reference Application
CMSIS_shield_header Shield configuration
STM32 HAL Drivers
CMSIS_device_header Processor and Peripherals
CMSIS-Driver API header files
Generator Bridge
CubeMX Generator
MX_Device.h
configuration information
*.c/*.h generated source files

## Slide 49
Generator Information
Generator Output
*.ioc Generator Project
*.c/*.h generated source files
<project>. cbuild-gen.yml
<project>. cgen.yml Import data for CMSIS-Toolbox
cbridge Generator Bridge
*.cbuild-gen-idx.yml
CubeMX Generator

## Slide 50: Configuration of Reference Applications
Initially contains empty target-type setting
solution:
cdefault:
target-types:
# Step 1: Specify your board, for example with: # - type: LPCXpresso54114
# board: NXP::LPCXpresso54114
# Step 2: Run `cbuild setup` and use cbuild-idx.yml to identify variables
# variables:
# - Board-Layer: ./layer/board/frdmk22f/frdmk22f.clayer.yml
# - Shield-Layer: ./layer/shield/agmp03/agmp03.clayer.yml
build-types:
- type: Debug
:
- type: Release
:
projects:
- project: ./freefall/fxls8962_freefall.cproject.yml
- project: ./freemaster_demo/fxls8962_freemaster_demo.cproject.yml
- project: ./interrupt/fxls8962_interrupt.cproject.yml
- project: ./normal/fxls8962_normal.cproject.yml
- project: ./normal_spi/fxls8962_normal_spi.cproject.yml
Command-line workflow:
User enters target type and specifies board in `csolution.yml`
User runs `cbuild setup` command, this generates `cbuild-idx.yml` with variable settings
  This command installs a potential missing BSP and DFP pack
  It delivers one or more potential configurations with variable settings
User selects on configuration and copies variable settings in `csolution.yml` which adds the layers
  Note: layers are not copied in this scenario and may be taken from pack location
IDE workflow:
User selects a reference example and specifies a board
IDE runs `cbuild setup` command, this generates `cbuild-idx.yml` with variable settings
  This command installs a potential missing BSP and DFP pack
  IDE shows one or more potential configurations
User selects a configuration
IDE copies variable settings from `cbuild-idx.yml` to `csolution.yml` which adds the layers
  Note: layers may be copied to csolution workspace and paths adjusted
IDE runs again `cbuild setup` command which completes the example configuration
  IDE shows the `settings` required for the example

## Slide 51: cbuild-idx.yml – variable settings
Potential content of cbuild-idx.yml for user configuration
build-idx:
generated-by: csolution version 2.4.0
cdefault: cdefault.yml
csolution: fxls8962.csolution.yml
configurations:
- configuration:
variables:
- Board-Layer: ./layer/board/frdmk22f/frdmk22f.clayer.yml
- Shield-Layer: ./layer/shield/agmp03/agmp03.clayer.yml
settings: - Board-Layer:
- set: Bus.SPI (FXLS8962 SPI Bus - Jumper configuration: I2C/SPI=SPI)
- set: Bus.SPI (FXAS21002 SPI Bus - Jumper configuration: I2C/SPI=SPI)
- configuration:
variables:
- Board-Layer: ./layer/board/frdmk22f/frdmk22f.clayer.yml
- Shield-Layer: ./layer/shield/fxls8962/fxls8961.clayer.yml