## Slide 1: CMSIS-Toolbox: Basis for next generation software tooling
Keil MDK – Version 6
Best-in-class embedded development system for Cortex-M microcontrollers
Command-Line and IDE workflows based on CMSIS-Toolbox
Arm C/C++ Compiler with FuSa certification
Based on CMSIS software standards
Host Support: Windows, Linux, Mac OS – and Cloud
Arm Virtual Hardware – FVPs
Precise simulation models of Cortex-M device sub-systems
Designed for complex software verification and testing
Enables test automation of diverse software workloads
Part of CI/CD and MLOps development flows
Supports A/B performance comparisons using CMSIS-View Event Recorder timing statistics
csolution project
Software Packs
CMSIS-Toolbox
cbuild: Build Invocation
Command-line workflow
Visual Studio Code IDE
Arm Virtual Hardware
Cortex-M0..M85
SIMD, Helium
Memory
DMA
Virtual I/O
Data Streaming
Ethos-U55/U65
microNPU
Peripherals
Ethernet, UART,…
Debug Interface
Event Recorder
Resources
microNPU
Test scripts
CI/CD integration
Integrations
Cloud Service
GitHub
Desktop tools
*.cproject.yml source files and SW components
Device/Board Generic Software
*.csolution.yml Target and Build Parameters

## Slide 2: Developer require flexibility
*.cproject.yml source files and SW components
Software Packs
Device/Board Generic Software
CMSIS-Toolbox
cbuild: Build Invocation
Command-Line and IDE Workflow + DevOps, MLOps, Config Tools, Git, …
Host Support: Windows, Linux, Mac OS – and Cloud
Compiler of choice: Arm Compiler 6, IAR, GCC, LLVM
csolution project
Command-line workflow
VS Code – CMSIS Solution Extension
*.csolution.yml Target and Build Parameters
Multiple IDEs: Keil uVision, IAR EW-Arm, NXP MCUXpresso, …

## Slide 3
Output Files
Input Files
Software Packs
*.rzone (optional) Defines system resources
*.csolution.yml Target (Device, Board) Build (Debug, Release)
*.cproject.yml Manages independent projects
Run-Time Environment (RTE) (*.c / *.h files with config information)
*.clayer.yml Defines re-usable project parts
Device Family Pack (DFP)
Defines device properties
Board Support Pack (BSP) Defines board properties
CMSIS Project Manager
Project Build Files *.cprj for CMSIS-Build
Generic Software Packs with drivers, middleware, etc.
Project Resource Files *.fzone for template engines
1
2
3
4
*.cdefault.yml Global Settings (Toolchain)

## Slide 4
Output Files
Input Files
Software Packs
*.rzone (optional) Defines system resources
*.csolution.yml Target (Device, Board) Build (Debug, Release)
*.cproject.yml Manages independent projects
Run-Time Environment (RTE) (*.c / *.h files with config information)
*.clayer.yml Defines re-usable project parts
Device Family Pack (DFP)
Defines device properties
Board Support Pack (BSP) Defines board properties
csolution CLI tool
Project Build Files *.cprj for CMSIS-Build
Generic Software Packs with drivers, middleware, etc.
Project Resource Files *.fzone for template engines
1
2
3
4
*.cdefault.yml Global Settings (Toolchain)
future extension
Generator
legacy
*.genlayer.yml Defines generated project parts
*.cbuild.yml Build information
future extension

## Slide 5
Default options for AC6, GCC, IAR, LLVM
Output Files
csolution project
Software Packs
*.csolution.yml Target (Device, Board) Build (Debug, Release)
*.cproject.yml Manages independent projects
Run-Time Environment (RTE) (config files*.c / *.h)
*.clayer.yml Defines re-usable project parts
Device Family Pack (DFP)
Defines device properties
Board Support Pack (BSP) Defines board properties
csolution CMSIS Project Manager
*.cbuild-idx.yml *.cbuild.yml
Build Information
Generic Software Packs with drivers, middleware, etc.
cdefault.yml Global Toolchain Settings
Note: Optionally memory information for Linker Scatter Files is generated.
Reproducible builds on different hosts
*.cbuild-run.yml Configuration for programmer and debugger
*.cbuild-pack.yml Pack version locking

## Slide 6
Generator Information
Generator Output
*.ioc Generator Project
*.c/*.h generated source files
<project>. cbuild-gen.yml
<project>. cgen.yml Import data for CMSIS-Toolbox
cbridge Generator Bridge
*.cbuild-gen-idx.yml
CubeMX Generator

## Slide 7
csolution CMSIS Project Manager
Debugger
Flash Programmer
OTA/Cloud Service
cbuild-set.yml Project context set

## Slide 8
Default compiler options for AC6, GCC, IAR
Output Files
csolution project
Software Packs
*.csolution.yml Target (Device, Board) Build (Debug, Release)
*.cproject.yml Manages independent projects
Run-Time Environment (RTE) (config files*.c / *.h)
*.clayer.yml Defines re-usable project parts
Device Family Pack (DFP)
Defines device properties
Board Support Pack (BSP) Defines board properties
cbuild CMSIS Project Manager
Generic Software Packs with drivers, middleware, etc.
cdefault.yml Global Toolchain Settings
*.cbuild-idx.yml *.cbuild.yml Build information
Note: Optionally memory information for Linker Scatter Files is generated.
*.cbuild-idx.yml *.cbuild.yml Build information

## Slide 9
Output Files
csolution project
Software Packs
*.rzone (optional) Defines system resources
*.csolution.yml Target (Device, Board) Build (Debug, Release)
*.cproject.yml Manages independent projects
Run-Time Environment (RTE) (*.c / *.h files with config information)
*.clayer.yml Defines re-usable project parts
Device Family Pack (DFP)
Defines device properties
Board Support Pack (BSP) Defines board properties
csolution CLI tool
Project Build Files *.cprj for CMSIS-Build
Generic Software Packs with drivers, middleware, etc.
Project Resource Files *.fzone for template engines
1
2
3
4
*.cdefault.yml Global Settings (Toolchain)
future extension
Generator
legacy
*.cgen.yml Defines generated project parts
*.cbuild.yml Build information
future extension

## Slide 10
Read previous *.cprj files to check for config file version changes
Control config file versions in case of updated software packs
Read Software Packs and csolution project files
Process data
Read previous *.cprj file to identify the config file versions previously used
Compare versions of “config” files, notify if updates are made (define rename process of config files)
Check if new *.cprj file is different from old config files; if it differs rename existing *.cprj to backup version; write new *.cprj file
Q: do we need a status file, perhaps for an IDE flow?
*.rzone (optional) that defines System Resources
*.csolution.yml Defines Target Application
*.cproject.yml Manages independent projects
Run-Time Environment (RTE) (*.c / *.h files with config information)
*.clayer.yml Defines re-usable project parts
Device Family Pack (DFP)
that defines Device Properties
Board Support Pack (BSP) that defines Board Properties
CMSIS Project Manager
Project Files *.cprj for CMSIS Build
csolution project
Software Packs
[default.]csettings.yml Global Settings (Toolchain, Device)
Generic Software Packs with drivers, middleware, etc.
Project Resource Files *.fzone for template engines
Output Files

## Slide 11: Multi-Project Build Process: IDE and CLI
*.csolution.yml Defines Target Application
csolution Project setup: defines tools, target, components, files, and current list of context that should be build.
csolution project
Build Control Files
*.cbuild-set.yml Defines context set of Application
cbuild (CLI)
Invokes csolution
When csolution project files are newer (context-set of *.cbuild-idx.yml defines scope) Invokes cbuild-gen for build process
<context>.cbuild.yml Build information for a project context
IDE
When setup in context manager is changed (or items modifed), csolution is called
When build is invoked, cbuild-gen is called.
Introduce `context-set`: defines the selected context for application
Items are stored in csolution project files
toolchain
device, board,
build-type, target-type
components
files
options
cbuild-gen
Build Process: uses the build control files to generate the output (via CMake, …)
csolution command-line defines context-set:
csolution convert HelloWorld.csolution.yml --context HelloWorld_cm0plus.Debug+FRDM-K32L3A6 --context -HelloWorld_cm4.Release+FRDM-K32L3A6

## Slide 12: Application Software – from Virtual to Physical Hardware
User Application Code
Virtual Layer
IoT/ML Software Platform
Provide evidence of correctness on Arm Virtual Hardware Target and Physical Hardware
Event Log file
User Application Code
Board Layer
IoT/ML Software Platform
Event Log file
Device SDK with configuration
User Application Code
Target Layer
IoT/ML Software Platform
Event Log file
Device SDK with configuration
More Software
More Drivers
Virtual Drivers
HW Drivers
Real I/O via test equipment
Real I/O via user peripherals
HW Drivers
Unit & Integration Testing on Virtual Hardware or Physical Hardware Boards
Deployment and System Testing on Production Hardware
Essentially the same event logs are generated across the different deployments. This ensures correctness.
Simulated I/O via Python scripts and stimuli files
Notes: Potential key customer: DSP Concepts. See email exchange:
From: Paul Beckmann <pbeckmann@dspconcepts.com> Sent: Wednesday, April 7, 2021 9:05 PM To: Reinhard Keil <Reinhard.Keil@arm.com> Subject: Re: Compiler comparison / Feedback on Audio API interface
Hi Reinhard,
We are our testing with MDK V5.31.0.0. Here is the detailed info:
For IAR, we used v8.50.1. For GCC, it was the version included with the ST tools. Not sure exactly which version this was.
We have done further benchmarking across different signal processing operations. I picked this one because it was a recent issue with a customer and highlights how GCC can be slow. For other kernels, the cycle counts are comparable.
Being able to run on the FVP would be very interesting for us. I see several advantages:
We can optimize and profile for cores before they are publicly available. For example, we are getting requests for M55 performance numbers but there are no announced CPUs.
Get accurate measurements of system level issues. Caching and memory accesses have a huge impact.
Could fit with our continuous integration plans so that we don't have to (always) test on external hardware.
We are speaking with Reed Hinkel about "cloud based profiling". I would like our customers to create a design in Audio Weaver and then upload the design to our website for profiling. They can select which processors to run on and then get detailed results showing where resources are consumed. The VFP would be ideal for this.
I also had one of my firmware engineers review the SAI interface. I'll provide all of his comments and you can see what is relevant:
It is well written and to make sure I understand it, low-level drivers must be written depending on the device.
  You have to kickstart the driver with calls to ARM_SAI_Receive() or ARM_SAI_Send() which are non-blocking.
  A callback function is registered during init called ARM_SAI_SignalEvent(event) which is called when the above completes with respective bits in the parameter "event" for each.
  ARM_SAI_Receive() or ARM_SAI_Send() mention that DMA is typical, but I am not sure if those two calls can be one time only and then the guts of the driver can provide calls to ARM_SAI_SignalEvent(event) on each DMA interrupt afterward. If yes, then it can work with our BSP's.
  The protocols cover about everything with User Defined Protocol allowing for generic TDM configuration.
    They are missing specification of left or right adjusted data and now to save captured data in memory. For instance if the data is 24-bits, is it saved right adjusted with sign extension or left adjusted?
    In general, you may capture even 16-bit data and want to save it in 32-bit memory left or right adjusted.
  The same API and supported protocols should include PDM (DMIC) input. The RT685 and NXP PDM IP in general have a means to convert to I2S, but that may not be on all parts and should not be necessary.
    Most devices have multiple stereo PDM ports that can capture data and send to two different DMA channels (left and right).
    This API seems to support single stream, interleaved, not multi-stream from one device. Is that correct?
  The documentation is not clear how you mask the TX event, bot allow the RX event and so on. Guessing it is in there.

## Slide 13: Multi-Project Requirements
Project D
Project B
Project A
Separate projects independently developed; combined in a multi-project workspace
Security
Storage
Crypto
Attestation
Device / Board HAL
RTOS
User Application
Cloud
Connector
Secure Network
Interface
Secure Boot
ML Library
ML Data
UX Graphic
Images
Control Algorithm
Processor #1
Processor #2
Project C

## Slide 14: Software Layers Group Pre-configured Software Components
RTOS Layer
App Layer
Socket Layer
IoT for Cortex-M – reference examples for many evaluation kits
Board Layer
MCU
Board
LED
Sensor inputs
Display
CMSIS-Driver-VIO
Virtual I/O
CMSIS-RTOS2
Example Application Code
Trusted Firmware-M (TF-M)
implements Security
Storage
Crypto
Attestation
Secure Boot
TrustZone Security
FreeRTOS, RTX, …
SPI
I2C
USART
WiFi
CMSIS-Driver
SPI, UART, (Ethernet)
Cloud Connector + Security
IoT Socket + Communication Stack
Peripherals covered by real CMSIS-Driver or VIO (Virtual I/O)
Timers
Analog
...
User Code
Specialized Peripherals
Device SDK with configuration
Module Layer
WiFi

## Slide 15: Scenarios to consider
csolution
cproject #1
cproject #2
clayer for common board settings
csolution
cproject #1 runs on CPU #1
cproject #2 runs on CPU #2
clayer #1 for board API
clayer #2 for board API
common RTE settings (includes generator files)
Projects that share a layer with common configuration
Layers that partly share a common configuration
RTE settings (includes generator files)

## Slide 16: CubeMX location of generated files
csolution
cproject #1
cproject #2
clayer directory
csolution
cproject #1 runs on CPU #1
cproject #2 runs on CPU #2
Require common directory for
generated files
“Simple” Projects that share a layer with common configuration
TrustZone or Multicore projects
./RTE/Device/$D contains generated files
csolution
csolution
cproject directory
./RTE/Device/$D contains generated files

## Slide 17: CubeMX location of generated files
clayer directory
csolution
cproject #1 runs on CPU #1
cproject #2 runs on CPU #2
Require common directory for
generated files
TrustZone or Multicore projects
clayer CPU #1
clayer CPU #2

## Slide 18: CSolution / CBuild: Generator Workflow
Steps for component selection and configuration
User selects components
in `*.cproject.yml` under `components:`
When this are components that require generation, user is notified about the requirement to run a generator and users the CSolution Run command.
Run a “Generator” for a list of components.
CSolution generates `*.cgen.yml` that provides the list of user-selected components.
User runs Generator
`*.cgen.yml` provides the input to the Generator with a list of selected components
Configuration is done.
  Interactive mode (where a settings file is generated)
  Remote mode (where a settings file is an input)
Generator creates the “myGen.gpdsc” that informs the CSolution tool about (a) the fact that a component is configured and has generated code, (b) additional components that are the result of some user configuration.
Discussion: is a component list or a dependency list
Generator might be VS Code plugin or web based.
User creates CBuild output with CSolution
Both `*.cproject.yml` “myGen.gpdsc” and read by Csolution and create the complete list of selected components.
If “myGen.gpdsc” does not contain component information about a component with `genId` that is selected in `*.cproject.yml` the generator configuration is incomplete. This can happen when a component is added at a later step.
Likewise the Generator should remove components that are no longer required. An indicator is needed. (NOT SOLVED YET)

## Slide 19: IoT Workshop Example - Structure
Reference Application Framework: map many applications to many boards
IoT Reference Application using RTOS Kernel
PSA Interface
Device/Board Abstraction Layer
Security Firmware
SW Building Blocks
Should come from multiple vendors. Requirement for standardized interface between the components (Open-CMSIS-CDI)
Reference Application: should be tested with a CI system against a standardized CDI framework
Should run (within reason) on many different existing v8M and v7M devices (TrustZone optional)
Should include OTA services with standardize interfaces
Future variants of the Framework should also support other application types (DSP, ML, Graphics)
Designed for `csolution` tool
Examples use Open-CMSIS-Pack and the csolution workflow with layers
Layer type names should be descriptive, i.e. board, socket, security
Examples are used to fine-tune the csolution workflow (see next slide)
Interface requirements between cproject/clayer files should be described
Final design is that layers are provided by software packs
Other Requirements:
Defined Startup/Call Sequence (see https://github.com/MDK-Packs/CB_Lab4Layer/tree/master/layer)
Example: https://github.com/MDK-Packs/CB_Lab4Layer/blob/master/layer/Board/MIMXRT1064-EVK/main.c
Socket Layer (IoT Socket -> WiFi or Ethernet)
CMSIS-Driver API
IoT Socket API
Objectives
Re-use existing packs from AWS and NXP
provide feedback when required
Define the overall structure of CMSIS-Packs, i.e. for
TF-M
mbedTLS
AVH Corstone-300 BSP
Board BSP (exemplified on STM32U5, NXP)

## Slide 20: Opportunity: Packs give flexibility to the SW Eco-system
Flexible Development Workflows with Open-CMSIS-Pack
Catalog of software packs
MyProject *.csolution.yml *.cproject.yml
Arm Virtual Hardware
+
Private software packs
+
CLI Tools
Support: Win/Linux/Mac
Integrate with: VS Code, Keil Studio Cloud
Other tool integrations:
Arm DS, Keil MDK, IAR EW-Arm, Eclipse
NXP?
ST?
Boards or Devices
AVH Integrates into:
CI, DevOps, MLOps systems (i.e. GitHub)
Keil MDK, Arm DS, IAR EW-Arm
Keil Studio Cloud
AVH Supports:
CI Validation
Evaluation
Training
Platform for Reference Applications:
Many different boards???
Standard Software exposed to developers:
Web portals
Inside IDEs
Confidential software
Git repo for development
Released software with versioning
CMSIS Toolbox
Compiler support
GCC
Arm Compiler
IAR Compiler
github.com/Open-CMSIS-Pack

## Slide 21: Linker Script File and Startup Code (Toolchain independent)
Linker Script File
C Preprocessor
Final Linker Input Script
A <regions>.h file specifies the available memory.
If this file does not exist, it is generated based on information in the software packs.
A Linker Script File can be provided using the `linker:` node.
If no Linker Script File is provided, compiler specific script file templates from .\ect directory of CMSIS-Toolbox are used.
<regions>.h Device (and Board) Memory Definitions

## Slide 22: Linker Script Management for Multi-Project Applications
Template Linker Script
Final Linker Script for Project A
<solution-name>+<target-name>.regions.h defines the memory layout for a complete solution. The file is in the folder .cmsis
This is a multi-project application specified in one *.csolution.yml file.
The template linker scripts are pre-processed to represent the final memory layout for each project.
<solution-name>+ <target>.regions.h
Global Memory Definitions
Final Linker Script for Project B
A toolchain specific linker script template is initially copied into the project .\RTE directory. The copy allows project-specific customization.
Template Linker Script for Project A
#define A_cproject
#define B_cproject
Template Linker Script for Project B

## Slide 23
RTE Directory
Project Area
csolution project
Software Packs
*.csolution.yml Target (Device, Board) Build (Debug, Release)
*.cproject.yml Manages independent projects
*.clayer.yml Defines re-usable project parts
csolution tool
*.pdsc Pack Metadata
*.cbuild.yml Build Information
*.cbuild-idx.yml Overall description with project index
Component Config Files
RTE_ components.h
Pre-include Files
Component Config Files
*.default.yml Compiler selection and toolchain default settings
cbuild2cmake tool called by cbuild
*.cbuild-set.yml context configuration
*.cbuild-pack.yml pack journal / lock

## Slide 24
*.cprj Build Information
cmakeLists.txt
compiler_name. <version>.cmake
CMake
build.ninja
Ninja
cbuildgen

## Slide 25
cbuild
cpackget
csolution
cbuild2cmake
CMake
Ninja
csolution project *.csolution.yml
*.cproject.yml
*.clayer.yml
Software Packs Device Family Pack
Board Support Pack
Generic Software Packs
Build Information list of source files, packs, tool options, etc.
User source code Configuration files Linker Scripts
Build Output Elf/Dwarf files Map files
etc.
Run and Debug Configuration for a complete target application

## Slide 26
Arduino Shield
D0
D1
D2
D3
D4
D5
D6
D7
D8
D9
D10
D11
D12
D13
GND
AREF
D20
D21
SDA
SCL
I2C
RXD
TXD
UART
D19
D18
D17
D16
D15
D14
VIN
GND
GND
+5V
+3V3
Reset
IOREF
NC
A5
A4
A3
A2
A1
A0
CIPO
SCK
SS
COPI
SPI
SCL
SDA
I2C-Alt
Analog
Digital
Communication

## Slide 27: Distribution of Reference Applications
Sensor SDK Pack
BSP Pack
Reference Application (<sensor>.csolution.yml / <sensor>.cproject.yml)
Layer Type: Board (<board-name>.clayer.yml)
Driver APIs
Layer Type: Shield (<shield-name>.clayer.yml)
Shield-specific API
Example: Sensor SDK Pack (github.com/RobertRostohar/NXP_Sensor_SDK) that contains:
Agnostic middleware for a sensor that is configurable (part of the Reference Application)
Board/Device agnostic examples that use this middleware (part of the Reference Application)
One or more Shield layers that provides configuration settings for the agnostic middleware
Board Layers are provided by a Board Support BSP Pack that is board specific
Sensor SDK Pack PDSC:
<example> describes Reference Application
<clayer> describes <shield-name>.clayer.yml
BSP Pack PDSC:
<clayer> describes <board-name>.clayer.yml

## Slide 29: IoT Workshop Example - Structure
Reference Application Framework: map many applications to many boards
Reference Application (*.cproject.yml)
PSA Interface
Layer Type: Board (<board-name>.clayer.yml)
Security Firmware
Layer Type: Socket Network Connectivity
CMSIS-Driver API
IoT Socket API
Layer Type: Shield (<shield-name>.clayer.yml)
Shield-specific API
Layer Type: RTOS RTOS Functionality
CMSIS-RTOS2 API
Layer Type: Stream Sensor Middleware
Data Stream API
Security Boundary

## Slide 30: Roadmap H1’2023 – CMSIS-Toolbox 2.0
Review proposals and agree on implementation timeline (until 15. Feb 2023)
Identify missing features for integration into VS Code
Work on Installer that (a) is stand-along for Linux, (b) installs CMSIS-Toolbox to VS Code
Define an overall multi-project workflow that starts from *.cbuild-idx.yml (as cbuild input file)
Complete Generator Workflow
Implement Gaps:
  csolution list config #142,
Out of scope (todo later in 2023)
CMSIS-Zone integration and resource management proposal
Command for batch delete #143

## Slide 31
Software Application
Software Packs
*.csolution.yml Target and Build Parameters
*.cproject.yml source files and SW components
csolution Project Manager
Device/Processor Information
Software Building Blocks

## Slide 32
User Application Code
Virtual Layer
IoT/ML Software Platform
Event Log file
User Application Code
Board Layer
IoT/ML Software Platform
Event Log file
Device SDK with configuration
User Application Code
Target Layer
IoT/ML Software Platform
Event Log file
Device SDK with configuration
More Software
More Drivers
Virtual Drivers
HW Drivers
Real I/O via test equipment
Real I/O via user peripherals
HW Drivers
Unit & Integration Testing on Virtual Hardware or Physical Hardware Boards
Deployment and System Testing on Production Hardware
Essentially the same event logs are generated across the different deployments. This ensures correctness.
Simulated I/O via Python scripts and stimuli files
Target Hardware Abstraction
Notes: Potential key customer: DSP Concepts. See email exchange:
From: Paul Beckmann <pbeckmann@dspconcepts.com> Sent: Wednesday, April 7, 2021 9:05 PM To: Reinhard Keil <Reinhard.Keil@arm.com> Subject: Re: Compiler comparison / Feedback on Audio API interface
Hi Reinhard,
We are our testing with MDK V5.31.0.0. Here is the detailed info:
For IAR, we used v8.50.1. For GCC, it was the version included with the ST tools. Not sure exactly which version this was.
We have done further benchmarking across different signal processing operations. I picked this one because it was a recent issue with a customer and highlights how GCC can be slow. For other kernels, the cycle counts are comparable.
Being able to run on the FVP would be very interesting for us. I see several advantages:
We can optimize and profile for cores before they are publicly available. For example, we are getting requests for M55 performance numbers but there are no announced CPUs.
Get accurate measurements of system level issues. Caching and memory accesses have a huge impact.
Could fit with our continuous integration plans so that we don't have to (always) test on external hardware.
We are speaking with Reed Hinkel about "cloud based profiling". I would like our customers to create a design in Audio Weaver and then upload the design to our website for profiling. They can select which processors to run on and then get detailed results showing where resources are consumed. The VFP would be ideal for this.
I also had one of my firmware engineers review the SAI interface. I'll provide all of his comments and you can see what is relevant:
It is well written and to make sure I understand it, low-level drivers must be written depending on the device.
  You have to kickstart the driver with calls to ARM_SAI_Receive() or ARM_SAI_Send() which are non-blocking.
  A callback function is registered during init called ARM_SAI_SignalEvent(event) which is called when the above completes with respective bits in the parameter "event" for each.
  ARM_SAI_Receive() or ARM_SAI_Send() mention that DMA is typical, but I am not sure if those two calls can be one time only and then the guts of the driver can provide calls to ARM_SAI_SignalEvent(event) on each DMA interrupt afterward. If yes, then it can work with our BSP's.
  The protocols cover about everything with User Defined Protocol allowing for generic TDM configuration.
    They are missing specification of left or right adjusted data and now to save captured data in memory. For instance if the data is 24-bits, is it saved right adjusted with sign extension or left adjusted?
    In general, you may capture even 16-bit data and want to save it in 32-bit memory left or right adjusted.
  The same API and supported protocols should include PDM (DMIC) input. The RT685 and NXP PDM IP in general have a means to convert to I2S, but that may not be on all parts and should not be necessary.
    Most devices have multiple stereo PDM ports that can capture data and send to two different DMA channels (left and right).
    This API seems to support single stream, interleaved, not multi-stream from one device. Is that correct?
  The documentation is not clear how you mask the TX event, bot allow the RX event and so on. Guessing it is in there.

## Slide 33
Target Hardware Abstraction
Target Hardware Abstraction

## Slide 34: Software components
A software component encapsulates a set of related functions.
Components should be substitutable by other components at design time.
Components can have dependencies on other components.
Software component
API headers
User code templates
Configuration files
Source code/
libraries
Documentation
Debug view
description
Interfaces to device peripherals or other software components
Interfaces to user application or other software components
  Provided Interfaces
  Required Interfaces
Notes: Requires you to think about the API of the software component

## Slide 35
- component: <2>
API header
Configuration files
Source code/
libraries
- component: <1>
API header
Configuration files
Source code/
libraries
- component: <1>
API headers
Configuration files
Source code/
libraries
Implementation #3
Implementation #2
Implementation #1
Source code/
libraries
Source code/
libraries
Source code/
libraries
Central API definition
API headers (Definition)
Documentation of API
- component: <2.C>
- component: <2.B>
- component: <2.A>
Source code/
libraries
Source code/
libraries
Source code/
libraries
Documentation
Notes: Requires you to think about the API of the software component

## Slide 36: Application example: TCP/IP network
Using network stack on STM32F407IG with internal MAC
Network:Socket:TCP
CMSIS Driver: Ethernet MAC
CMSIS Driver: Ethernet PHY
Network:Interface:ETH
Network:CORE
CMSIS:CMSIS-RTOS
Device Family Pack
Middleware Pack
CMSIS Pack
External Driver Pack
CMSIS:CORE
Device:Startup

## Slide 37: Class / Pack view
Device - pack vendor::DFP
CMSIS - pack Arm::CMSIS
CMSIS-Driver - pack vendor::HAL-Interface
CMSIS-Driver - pack Arm::CMSIS-Driver
CMSIS:RTOS2 RTOS&FreeRTOS - pack Arm::CMSIS-FreeRTOS
Network - pack: lwIP::lwIP
IoT Utility - pack MDK-Pack:IoT-Socket
IoT Client

## Slide 38: Software components – Taxonomy
Software component have these attributes that are used to identify them:
  Component Class (Cclass): examples are CMSIS, Device, File System
  Component Group (Cgroup): examples are CMSIS:RTOS, Device:Startup, File System:CORE
  Component Version (Cversion): the version number of the software component
Optionally, a software component may have additional attributes:
  Component Sub-Group (Csub): examples are CMSIS:RTOS:MyRTOS, Device:Driver USBD:Full-speed
  Component Variant (Cvariant): a variant of the software component: RTOS:FreeRTOS
  Component Vendor (Cvendor): the supplier of the software component
Notes: Requires you to think about the API of the software component

## Slide 39: Bundles
A bundle is a variant on the Cclass level.
It specifies the attributes Cclass, Cversion and optionally Cgroup and Cvendor for a collection of interdependent components.
Components within a bundle inherit the attributes set by the bundle and must not set these attributes again.
Bundles ensure consistency of attributes across multiple interworking components and restrict the mix and match of components within a Cclass from different solutions.
Bundle
Component A
Component B
Component C
Component X
Component Y
Component Z
Notes: Requires you to think about the API of the software component

## Slide 40: Bundles
In case multiple inter-dependent components that belong to the same Cclass form part of a solution, these can be grouped into a bundle (Cbundle).
A Cbundle specifies identical attributes Cclass, Cversion and optionally Cgroup and Cvendor for several components.
Components within a bundle inherit these attributes set by the bundle and cannot alter these attributes (for example component version).
Bundles ensure consistency of attributes across multiple interworking components and restrict the mix and match of components within a Cclass from different software packs.

## Slide 41: Relationships of packs and software components
Packs can require other packs to be available:
Components can have dependencies on other components; either from the same or from other packs:
Pack A
Version n
Pack B
Version m
Pack A, Version n
Component A
Component B
Component C
Pack B, Version m
Component A
Component B
Component C

## Slide 42: Central API Interface definition for software components
Implementation #3
Implementation #2
Software
component
Central API definition
A common problem: API headers evolve over time.
A central API definition shares header file and documentation of an API interface across multiple other software components to ensure consistency.
The API interface is distributed separate or as part of the software component that consumes this interface. The API header file is therefore.
An example is the CMSIS-Driver pack that contains various Ethernet and Flash drivers – all compatible with the CMSIS-Driver APIs that are published in the CMSIS Pack.
API headers
Source code/
libraries
Interfaces
API headers (Definition)
Implementation #1
Source code/
libraries
Source code/
libraries
Source code/
libraries
Documentation of API
Notes: Requires you to think about the API of the software component

## Slide 43: API components
An API is a special form of a software component that only defines a C/C++ Application Programming Interface (API).
An API does not contain the actual implementation (usually provided by source code or library files) and cannot be selected in a development tool. One example is the CMSIS-RTOS API, which is specified as part of CMSIS. However, the actual RTOS implementation is provided by different vendors.
An API consists of a name, a brief description as well as one or more header files. It references a document containing the specification of the API.

## Slide 44: Application example: TCP/IP network
Using network stack on STM32F407IG with internal MAC
Network:Socket:TCP
Ethernet MAC
Ethernet PHY
Network:Interface:ETH
Network:CORE
CMSIS:CMSIS-RTOS
Vendor 1 Pack
Middleware Pack
CMSIS Pack
External Driver Pack
CMSIS:CORE
Device:Startup

## Slide 45: Application example: TCP/IP network
Using network stack on an NXP LPC54108 without MAC
- component: Network:Socket:TCP
Ethernet MAC and PHY
CMSIS-Driver SPI
- component: Network:Interface:ETH
- component
Network:CORE
- component: CMSIS:CMSIS-RTOS2:RTX
- pack: Device Family Pack
- pack: Middleware Pack
- pack: CMSIS Pack
- pack: External Driver Pack
- component: CMSIS:CORE
Device:Startup

## Slide 46: Managing software components in a project
Pack manager creates RTE_Components.h header file
RTE_Components.h is an inventory file that contains:
CMSIS_device_header #define for generic access to the selected device’s header file
All defines that are generated out of components from PDSC files:
<component Cgroup="Core" Cversion="10.0.1" condition="FreeRTOS"> <description>Core components API (Kernel, Tasks, Semaphores, Mutexes, Queues)</description> <RTE_Components_h> #define RTE_RTOS_FreeRTOS_CORE /* RTOS FreeRTOS Core */ </RTE_Components_h> . . . </component>
Is added to the RTE_Components.h file:
/* * Auto generated Run-Time-Environment Component Configuration File * *** Do not modify ! *** */ #ifndef RTE_COMPONENTS_H #define RTE_COMPONENTS_H /* Define the Device Header File: */ #define CMSIS_device_header "ARMCM3.h“ #define RTE_RTOS_FreeRTOS_CORE /* RTOS FreeRTOS Core */ #endif /* RTE_COMPONENTS_H */

## Slide 47: Distribution of Reference Applications
Sensor SDK Pack
BSP Pack
Reference Application (<sensor>.csolution.yml / <sensor>.cproject.yml)
Layer Type: Board (<board-name>.clayer.yml)
Driver APIs
Layer Type: Shield (<shield-name>.clayer.yml)
Shield-specific API
Example: Sensor SDK Pack (github.com/RobertRostohar/NXP_Sensor_SDK) that contains:
Agnostic middleware for a sensor that is configurable (part of the Reference Application)
Board/Device agnostic examples that use this middleware (part of the Reference Application)
One or more Shield layers that provides configuration settings for the agnostic middleware
Board Layers are provided by a Board Support BSP Pack that is board specific
Sensor SDK Pack PDSC:
<example> describes Reference Application
<clayer> describes <shield-name>.clayer.yml
BSP Pack PDSC:
<clayer> describes <board-name>.clayer.yml

## Slide 48: Distribution of Reference Applications
MDK Middleware Pack
BSP Pack
Reference Application Example
Layer Type: Board (<board-name>.clayer.yml)
Driver APIs
USB Device
RTOS
HID Class
CMSIS-View
connections:
- connect: USB Device HID
consumes:
- CMSIS_USB_Device
- CMSIS_VIO
connections:
- connect: Board with USB
provides:
- CMSIS_USB_Device
- CMSIS_VIO

## Slide 49: Header File Structure
CMSIS_target_header Driver configuration
Device Registers
Reference Application
Hardware Abstraction
Driver implementation
Driver API Shim Interface
CMSIS_shield_header Shield configuration
CMSIS_target_header Driver configuration
Device Registers
Reference Application
CMSIS_shield_header Shield configuration
CMSIS_device_header Processor and Peripherals
STM32 HAL Drivers
CMSIS_device_header Processor and Peripherals
CMSIS-Driver API header files
CMSIS-Driver API header files

## Slide 50
Driver API Shim Interface
CMSIS_target_header Driver configuration
Device Registers
Reference Application
CMSIS_shield_header Shield configuration
STM32 HAL Drivers
CMSIS_device_header Processor and Peripherals
CMSIS-Driver API header files
Generator Bridge
CubeMX Generator
MX_Device.h
configuration information
*.c/*.h generated source files

## Slide 51
Generator Information
Generator Output
*.ioc Generator Project
*.c/*.h generated source files
<project>. cbuild-gen.yml
<project>. cgen.yml Import data for CMSIS-Toolbox
cbridge Generator Bridge
*.cbuild-gen-idx.yml
CubeMX Generator

## Slide 52: Configuration of Reference Applications
Initially contains empty target-type setting
solution:
cdefault:
target-types:
# Step 1: Specify your board, for example with: # - type: LPCXpresso54114
# board: NXP::LPCXpresso54114
# Step 2: Run `cbuild setup` and use cbuild-idx.yml to identify variables
# variables:
# - Board-Layer: ./layer/board/frdmk22f/frdmk22f.clayer.yml
# - Shield-Layer: ./layer/shield/agmp03/agmp03.clayer.yml
build-types:
- type: Debug
:
- type: Release
:
projects:
- project: ./freefall/fxls8962_freefall.cproject.yml
- project: ./freemaster_demo/fxls8962_freemaster_demo.cproject.yml
- project: ./interrupt/fxls8962_interrupt.cproject.yml
- project: ./normal/fxls8962_normal.cproject.yml
- project: ./normal_spi/fxls8962_normal_spi.cproject.yml
Command-line workflow:
User enters target type and specifies board in `csolution.yml`
User runs `cbuild setup` command, this generates `cbuild-idx.yml` with variable settings
  This command installs a potential missing BSP and DFP pack
  It delivers one or more potential configurations with variable settings
User selects on configuration and copies variable settings in `csolution.yml` which adds the layers
  Note: layers are not copied in this scenario and may be taken from pack location
IDE workflow:
User selects a reference example and specifies a board
IDE runs `cbuild setup` command, this generates `cbuild-idx.yml` with variable settings
  This command installs a potential missing BSP and DFP pack
  IDE shows one or more potential configurations
User selects a configuration
IDE copies variable settings from `cbuild-idx.yml` to `csolution.yml` which adds the layers
  Note: layers may be copied to csolution workspace and paths adjusted
IDE runs again `cbuild setup` command which completes the example configuration
  IDE shows the `settings` required for the example

## Slide 53: cbuild-idx.yml – variable settings
Potential content of cbuild-idx.yml for user configuration
build-idx:
generated-by: csolution version 2.4.0
cdefault: cdefault.yml
csolution: fxls8962.csolution.yml
configurations:
- configuration:
variables:
- Board-Layer: ./layer/board/frdmk22f/frdmk22f.clayer.yml
- Shield-Layer: ./layer/shield/agmp03/agmp03.clayer.yml
settings: - Board-Layer:
- set: Bus.SPI (FXLS8962 SPI Bus - Jumper configuration: I2C/SPI=SPI)
- set: Bus.SPI (FXAS21002 SPI Bus - Jumper configuration: I2C/SPI=SPI)
- configuration:
variables:
- Board-Layer: ./layer/board/frdmk22f/frdmk22f.clayer.yml
- Shield-Layer: ./layer/shield/fxls8962/fxls8961.clayer.yml

## Slide 54: Developers want project examples
Board Support Pack (BSP)
Examples that run on a board
Board specific Template Projects
Board Layer with HAL drivers
Kick start application development with easy to access usage examples
Device Family Pack (DFP)
Device Specific Template Projects
Generic Software Pack (GSP)
Examples that run on a board
Reference Applications
Code Templates for components
RTOS
Graphic
CANopen
Example projects that run on eval boards
A csolution project may group similar examples
Examples for a board can be in different packs
Template projects are user application stubs
Pre-configured for different use cases
Code Templates for software components
Shows how to use a software component
Reference Applications - hardware agnostic
Require HAL driver interfaces to run
Board Layer with HAL drivers
Provides HAL driver interfaces
Notes: Today, developers rely on example projects to kick start their application development. In the Open-CMSIS-Pack system, we pay a lot of attention on meaningful examples that are easy to access.
All of this is based on CMSIS-Packs. There are different flavors that can provide various types of examples.
Device family pack can provide device specific template projects.
Board support packs obviously contain examples that run on on a specific board. But also board specific template projects that are preconfigured for different application types. BSPs can also have board layers with driver interfaces for certain use cases.
Middleware packs contain preconfigured examples that run out of the box on a give board for software such as an RTOS, or a graphics pack that we show today. IN the next we episode of this series, we will be looking at the CANopen stack from EmSA. Reference applications are hardware agnostic and require driver interfaces that are provided via board layers. Packs can also contain user code templates which give you a starting point for using a software component.
To make it easy, we have several ways. On the website you can see all the different packs. And the boards that they support along with examples.
In VS Code, us the Create-new-solution flow. Once you select a board, it shows the examples available.
You have also access to templates or reference applications. You can also have several csolution examples that run directly on this board. It’s really easy to get started.
For the user code templates, we have a similar way. You add a new file and choose the option “code template”.
BTW, all of this works in VS Code and µVision similarly and Embedded Wizard will now show how example examples show the rich feature set of their graphics middleware and how they help customers with a starting point for their own projects.
Manuel, Tim, the stage is yours.

## Slide 55
*.cproject.yml source files and SW components
Software Packs
Device/Board Generic Software
CMSIS-Toolbox
cbuild: Build Invocation
VSCode Extension
CMSIS-Solution
csolution project
My.csolution.yml Target and Build Parameters
output
ELF/DWARF HEX/binary files
Run
Debug
My+target. cbuild-run.yml Run and Debug Configuration
*.dbgconf Device configuration for Debug/Trace
pyOCD VSCode Extension
CMSIS-Debug
User created input files
Generated output files
Open-CMSIS Tools
Published software packs

## Slide 56
*.cproject.yml source files and SW components
Software Packs
Device/Board Generic Software
CMSIS-Toolbox
cbuild: Build Invocation
VSCode Extension
CMSIS-Solution
csolution project
My.csolution.yml Target and Build Parameters
output
ELF/DWARF HEX/binary files
Run
Debug
My+target. cbuild-run.yml Run and Debug Configuration
*.dbgconf Device configuration for Debug/Trace
pyOCD VSCode Extension
CMSIS-Debug
West / CMake
Zephyr Project Managed with KConfig
ELF/DWARF HEX/binary files

## Slide 57: Run and Debug Management: pyOCD implementation
CMSIS project or West build Application Images
Software Packs
Device/Board Parameters
CMSIS-Toolbox
cbuild: Build Invocation
VSCode Extension
CMSIS-Solution
csolution project
My.csolution.yml Target and Build Parameters
output
ELF/DWARF HEX/binary files
Run
Debug
My+target. cbuild-run.yml Run and Debug Configuration
*.dbgconf Device configuration for Debug/Trace
pyOCD VSCode Extension
CMSIS-Debug
User created input files
Generated output files
Open-CMSIS Tools
Published software packs
A single file `*cbuild-run.yml` contains all relevant information for run and debug of an application.
pyOCD command-line
  > pyocd list --cbuild-run MyProject+TargetHW.cbuild-run.yml // details of debug connection (scan JTAG, SWD)
  > pyocd gdbserver --cbuild-run MyProject+TargetHW.cbuild-run.yml // start debug server, load command: flash
  > pyocd load --cbuild-run MyProject+TargetHW.cbuild-run.yml // flash and run application
  > pyocd erase --cbuild-run MyProject+TargetHW.cbuild-run.yml // erase image on device

## Slide 58
Application
Board Layer for STM32F746G Disco
Board Layer for Production
Hardware
Test Case Project
Layer for Hardware Board
Layer for Simulation Model
Test Case Project
Test Case Project

## Slide 59: Using Layers for Middleware Examples
MDK Middleware Example
Board Layer for STM32F746G Disco
Board Layer for CustomHW
Notes: Thank you Hans for this interesting demo. Let me recap what he did. This is the Manual section of the CMSIS Toolbox that talks about the MDK Middleware Reference Applications. As has did explain several Board Support packs contain such layers. The CMSIS Toolbox uses connections to identify compatible layers.
You can see here, the connections of the Reference example and the board layer match. This makes it possible to use this board layer to run the example application. The board layer can however have more connections, which allows you to use this layer for many other different applications. This is how we scale in future our example projects to different evaluation boards.
All you need as a board vendor is to ship a board layer with the right scope of connections in a board support pack.
Now, Hans used the STM32F746G Disco board, and the tool gave him the right layer for his example. He could have then development the application software by still using the evaluation kit.
This speeds up development as you need not to wait for the production hardware. But once this custom hardware arrives, you may just add another board layer to your application.
Now you can continue using both the evaluation kit and the custom hardware for software development.
But with this layer concept you can do a lot more.

## Slide 60: Using Layers for test automation
Unit test and software test on hardware or simulation models
github.com/Arm-software/AVH
Test Case Project
Layer for Hardware Board
Layer for Simulation Model
Test Case Project
Test Case Project
Notes: Layers provide flexibility for many different use cases.
This diagram shows the structure of a test case project that uses layers to run on hardware or simulation models. Both layers provide effectively the same API interface. The difference is that the layer for the simulation model provides virtual interfaces that allow you for example to connect to I/O streams. Using the Virtual Streaming Interface gives you for example access to sensor data, audio or video files.
We provide several examples as developer resources for our Arm Virtual Hardware that you can find on GitHub. Here is a list of examples that includes a simple Hello World, a CI template to create own unit test projects, or VSI examples. We are using CI tests for many CMSIS components and also these repositories are public.
Potentially show AVH github + MQTT github

## Slide 61: Using Layers to add Hardware Shields
github.com/Open-CMSIS-Pack/Sensor-SDK
Sensor SDK Pack
BSP Pack
Reference Application (<sensor>.csolution.yml / <sensor>.cproject.yml)
Layer Type: Board (<board-name>.clayer.yml)
Driver APIs
Layer Type: Shield (<shield-name>.clayer.yml)
Shield-specific API
MEMS Sensor
The VS Code – CMSIS Solution combines layers for you
Notes: Layers can also simplify evaluation of hardware. Here we show an NXP Sensor Arduino shield. Obviously, the hardware connects easily to microcontroller boards that offer Arduino connectors. But how can we offer evaluation software for many different boards?
The VS Code CMSIS solution helps here. It can combine the software part of a Sensor SDK that contains a reference application for the sensor with a Board layer of an evaluation kit that supports Arduino interfaces. The tool picks for you the right layers and even provides information about jumper settings that you should apply to make it work.
The software itself is retargeted using the Shield layer that provides effectively a header file with the pin mapping of the Arduino shield. If you want to use the same software components on production hardware without Arduino connector – all you need is a different pin mapping header file in your layer.
Again, we provide this example on GitHub.

## Slide 62
*.cproject.yml source files and SW components
Software Packs
Device/Board Generic Software
csolution Server Mode
csolution project
My.csolution.yml Target and Build Parameters

## Slide 63
SoC
GDB Server (i.e. pyOCD)
Debug Adapter CMSIS-DAP JLink
Etc.
Cortex Processor core #2
Cortex Processor core #1
JTAG SWD
GDB Server Port Processor core #1
GDB Server Port Processor core #2
Each processor core is assigned to one GDB Server Port

## Slide 64: Telnet service for character I/O (stdio)
VS Code / pyOCD Debugger setup
Processor #1
Target System
Processor #1
Use `printf` messaging via debug connection (with no separate UART)
Semihosting (C library feature using breakpoints) or retargeting via SEGGER RTT (for higher bandwidth).
Features for regression testing: Text File output or Telnet Server connection
VS Code Serial Monitor connects to both UART or Telnet service
Semihosting
RTT mode: stdio
Processor #n
Semihosting
RTT mode: stdio
Processor #n
Console
Serial Monitor
Telnet Server
Text File
Console
Serial Monitor
Telnet Server
Text File
…
…
Manage Solution Settings

## Slide 65: RTT: Real-Time Transfer for I/O and system monitoring
Target System
Processor #1
RTT channel #0 Serial I/O
RTT channel #1 SDSIO Interface
Processor #n
RTT channel #0 Serial I/O
RTT channel #1 SystemView
…
YML setup example
Modes:
Setup

## Slide 66: Connect SDS-Framework with MLOps Systems
CMSIS projects or West builds Generate muliple application Images
Device Family Pack
CMSIS-Toolbox
cbuild: Build Invocation
VSCode Extension
CMSIS-Solution
csolution project
MyApp.csolution.yml MLOps configuration for hardware target and simulation model
output
MyApp.cbuild-mlops.yml Vela options for model
Build and test parameters for hardware & simulation
MLOps System VSCode Extension
CMSIS-Debug
User created input files
Generated output files
Development Tools
Published software packs
A single file `*cbuild-mlops.yml` contains all information to generate and validate ML models using SDS-Framework
MLOps Parameters:
Vela.ini configuration
Model Deployment:
Linker script
ML Model

## Slide 67: Trace for heterogenous multi-core systems
Configure trace communication
Uses Corsight components for run-time analysis with IDE and CLI for DevOps & AI agents
Configure trace generation
Collect trace information
Analyze trace data files
Combine Trace communication settings with DFP Information
CMSIS-Toolbox
Manage Solution Dialog
CMSIS Solution
VS Code Extension
Trace Generation Setup View
CMSIS Debugger
VS Code Extension
Trace Viewer + Trace Server CMSIS Debugger
VS Code Extension
Configure Target and Collect Trace pyOCD
Trace Communication Setup My.csolution.yml
<target-set>.dbgconf
<target-set>.cbuild-run.yml
Convert Trace Generation Setup to Corsight Register Values
pyTS
Trace Generation Setup <target-set>.ctrace.yml
Raw Trace Stream <target-set>.SWOraw
<target-set>.ctrace-run.yml
Trace Decoder OpenCSD + Writer CTF Converter
IDE Components
Command-Line Tools
Image Files
ELF/DWARF + HEX
CTF Files
Trace Data CSV
Configuration files (user setup)
Generated files
Notes: This slide explains how we develop features like trace for interactive usage in IDE, but also for CLI usage in DevOps systems and the era of Agentic AI. Agentic AI splits tasks into small steps; called skills. These skills are likewise relevant for IDE usage. This slide shows four skills required for trace. All the information is clearly stored in machine readable data files. (YML files are used for configuration which is easy to read by machines and humans).
And these “skills” are integrated into the IDE for interactive usage, but also available as command-line tools for DevOps and Agentic AI